## Slide 1: System for Automatic Greenhouse Vlad VELICIU, Conf.Dr.Ing. Liviu VIMAN

## Slide 2: Content
Introduction
Hardware Implementation
Software Implementation
Results
Conclusions

## Slide 3: Introduction
Measured parameters:
air temperature, air humidity
light intensity
NO2, NH3, CO concentration
soil parameters (temperature, moisture, PH, Nitrogen, Phosphorus, Potassium)
Water pump and Light control
4-layer PCB
Wi-Fi communication

## Slide 4: Hardware Implementation
ATmega-64A:
8-bit AVR
RISC architecture
Operating supply: 3V3
Operating frequency: 8MHz
ICSP

## Slide 5: Soil Quality sensor - RS485 communication
Fail-safe configuration:
Differential (120 Ohm), half-duplex
Driver min voltages
Receiver min voltages

## Slide 6: Optocoupling of RS485 communication
Transceiver MAX485
Symmetrical resistances to increase CMRR
Reduce power on the transistor

## Slide 7: Optocoupling of RS485 communication
Simulations (for RO)

## Slide 8: Gas concentration sensor
Analog, metal-oxide
Heating:
20 samples for each gas collected every 66ms
Rs/Ro vs concentration characteristics known (logarithmic)

## Slide 9: Gas concentration sensor
Linearization of Rs/Ro vs ppm characteristic
  Ro_CO = 2kΩ → 8ppm
  Ro_NO2 = 50.25kΩ → 0.22ppm

## Slide 10: I2C sensors
Temperature and Humidity sensor HS3002
Light intensity sensor BH1721FVC
2.2 kOhm pull-up resistors on the bus
HS3002
BH1721FVC

## Slide 11: Water Pump Control
Resistance in the base of Q2:
Max current for the pump: 300mA
Schottky diode to reduce spikes on the transistor
PWM command with frequency 120Hz

## Slide 12: Light Control
Relay control
Resistance in the base of Q4:

## Slide 13: Water Pump Control and Light Control
Simulation:
Without Schottky Diode
With Schottky Diode

## Slide 14: Water Level Sensor
Analog sensor (2.5V at high level)
Noninverting hysteresis comparator
  After calculations:

## Slide 15: Water Level Sensor
Simulation (WATER_LEVEL vs Signal from Sensor):

## Slide 16: Water Level Sensor
Functioning of the external interrupt in Proteus:

## Slide 17: Power Supplies
2*3.7V (6.8Ah) Li-Ion Batteries for each
LD1117DT33CTR for 3.3V
L7805CD2T-TR for 5V

## Slide 18: Power Supplies – Thermal design
3V3:
9 VIAs
5V:
20 VIAs

## Slide 19: PCB design
Stack-up:

## Slide 20: PCB design
Guarding of I2C bus and oscillator
Galvanic isolation
Signal trace width: 0.3mm (50 Ohm)
Differential pair (120 Ohm) width: 0.12mm / gap: 0.2mm
Power trace width: 0.4mm + polygons
Cut-out Area for ESP-12E
Stitching GND Vias
Bypass and decoupling capacitors

## Slide 21: PCB design
Guarding of I2C bus and oscillator
Galvanic isolation
Signal trace width: 0.3mm (50 Ohm)
Differential pair (120 Ohm) width: 0.12mm / gap: 0.2mm
Power trace width: 0.4mm + polygons
Cut-out Area for ESP-12E
Stitching GND Vias
Bypass and decoupling capacitors

## Slide 22: Software Implementation

## Slide 23: Duty Cycle control
Fuzzy Logic System – Takagi-Sugeno degree 0

## Slide 24: Duty Cycle control
Fuzzy Logic System – Takagi-Sugeno degree 0
Changing input sets:
Byte | Chosen desired temperature / humidity | Desired temperature / humidity used for the fuzzy controller
6 / 11 | < 20°C / < 30% | 12°C / 18%
7 / 12 | [20°C; 30°C) / [30%; 55%) | 25°C / 42%
8 / 13 | [30°C; 40°C) / [55%; 70%) | 35°C / 62%
9 / 14 | [40°C; 55°C) / 70% | 48°C / 80%
10 | 55°C | 77°C
Byte | Chosen desired temperature / humidity | Desired temperature / humidity used for the fuzzy controller
6 / 11 | < 20°C / < 30% | 12°C / 18%
7 / 12 | [20°C; 30°C) / [30%; 55%) | 25°C / 42%
8 / 13 | [30°C; 40°C) / [55%; 70%) | 35°C / 62%
9 / 14 |  | 48°C / 80%
10 |  | 77°C

## Slide 25: Experimental Results
1 – LCD
2 – MICS-6814
3 – ATmega64A
4 – I2C sensors (HS3002, BH1721)
5 – ESP-12E
6 – RS-485 transceiver circuit
7 – circuit for water level sensor
8 – water pump control circuit
9 – light control circuit
10 – 5V supply (LDO and battery header)
11 – 3.3V supply (LDO and battery header)
12 – soil quality sensor
13 – water pump
14 – water level sensor

## Slide 26: Experimental Results
HS3002: 64.59% humidity and 28.86°C

## Slide 27: Experimental Results
BH1721: 10lx

## Slide 28: Experimental Results
RS485 signals:
Data Bytes transmitted
Data Bytes received

## Slide 29: Experimental Results
Water Level sensor

## Slide 30: Experimental Results
Water Pump control

## Slide 31: Experimental Results
ThingsBoard Interface
Structure of an RPC call

## Slide 32: Conclusions
System used for monitoring and control
Simple system
Vital parameters for greenhouse
Accessible via Wi-Fi
From everywhere
Permanent monitoring and control
Further improvements:
More parameters to control
Solar panel supplies

## Slide 33: Thank you! Q&A